## Slide 1: Validation of DynaFlow versus Hades
Training Session: Preparing the BASECASEs for the Pipeline
February 17, 2022
Dynaωo

## Slide 2: Summary for DynaFlow (for Dynawo vs. Hades)
Follow the dynawo-validation-AIA/src/dynawo_validation/doc/README_INSTALLATION.md to install the package
Start from a case that both Dynawo & Hades run OK
Initial directory structure:
  Hades case under Hades subfolder, with input filename pattern: donneesEntreeHADES2.xml
  Dynawo case at first level, with job filename pattern: *JOB*.xml
Re-indent all XML files with xmllint --format  helper script: xml_format_dir.sh
Prepare the JOB file:
  edit the simulation stopTime (double it, for the disconnection)
  enable the PF output (`<dyn:finalState exportIIDMFile="true" exportDumpFile="false"/>`)
  enable the constraints file (`<dyn:constraints exportMode="XML"/>`)
  enable the timeline file (`<dyn:timeline exportMode="XML"/>`)
  enable the curves file (`<dyn:curves inputFile=”casename.crv" exportMode="CSV"/>`)
  set the desired log level ("DEBUG" is too verbose for a full contingency run)

## Slide 3: Summary for DynaFlow (for Dynawo vs. Hades)
Introduce a dummy disconnection in DynaFlow:
  this will become the reference for the disconnection time for all contingencies
  typically, set the disconnection event at t=100 and the stopTime at t=200
  To do this, we must first modify the JOB file with the helper script included in the package (add_contg_job.py). This script will add a reference to a new (very small) dyd file, so that we leave the entire old dyd untouched.
  Next, we need to create two new files. They must be called contingency.par and contingency.dyd.
    In the dyd file, introduce a disconnection model.
    In the par file, introduce the corresponding parameters of that disconnection.
Create a curves file, which is useful for inspecting the time-domain response
  you don't need to actually configure any curves, but you'll need at least an empty file because the scripts that generate the contingency cases will *add* curves to it.

## Slide 4: Summary for DynaFlow (for Dynawo vs. Hades)
Example:
In bold, expected names (i.e. hard-coded)
The job file is a pattern ‘*JOB*.xml’
Note: file extensions are also assumed as shown here (both *.iidm and *.xiidm are accepted). The core pipeline does not depend on this anymore, but other helper scripts to (e.g. convert_dflow2dwoAdwoB.sh)
20210422_0930a.BASECASE/
├── contingency.dyd
├── contingency.par
├── Hades
│ └── donneesEntreeHADES2.xml
├── JOB.xml
├── Network.par
├── recollement_20210422_0930.crv
├── recollement_20210422_0930_Diagram/
├── recollement_20210422_0930.dyd
├── recollement_20210422_0930.par
├── recollement_20210422_0930.iidm
└── solver.par

## Slide 5: Summary for DynaFlow (for Dynawo vs. Dynawo)
For Dynawo vs. Dynawo, first perform all the steps as in the Hades vs. Dynawo case, and then:
Use the utility scripts convert_dflow2dwoAdwoB.sh to convert the case into a new subdirectory structure A / B:
Manually perform whatever changes are desired to case A and/or B

## Slide 6: Summary for DynaFlow (for Dynawo vs. Dynawo)
Example:
20210422_0930a.BASECASE.DWODWO/
├── A
│ ├── contingency.dyd
│ ├── contingency.par
│ ├── Network.par
│ ├── recollement_20210422_0930.crv
│ ├── recollement_20210422_0930_Diagram
│ ├── recollement_20210422_0930.dyd
│ ├── recollement_20210422_0930.par
│ ├── recollement_20210422_0930.xiidm
│ └── solver.par
├── B
│ ├── contingency.dyd
│ ├── contingency.par
│ ├── Network.par
│ ├── recollement_20210422_0930.crv
│ ├── recollement_20210422_0930_Diagram
│ ├── recollement_20210422_0930.dyd
│ ├── recollement_20210422_0930.par
│ ├── recollement_20210422_0930.xiidm
│ └── solver.par
├── JOB_A.xml
└── JOB_B.xml

## Slide 7: Summary for DynaWaltz (for Dynawo vs. Astre)
Start from a case where both Dynawo & Astre run OK
Initial directory structure:
  Astre case under Astre subfolder, with input filename pattern: donneesModelesEntree.xml
  Dynawo case at first level, with job filename pattern: *JOB*.xml
Re-indent all XML files with xmllint --format  helper script: xml_format_dir.sh
Run the Dynawo case, then keep the t0 output and erase the tFin output
Create or complete the curves file, for both Astre and DynaWaltz
  Use helper script prepare_pipeline_basecase.py (creates a standardized, RTE-specific set of curves)
Prepare the JOB file:
  comment out the t0 job altogether.
  in the tFin job, edit the path to the t0 results. Example:
    < <initialState file="t0/outputs/finalState/outputState.dmp"/>
    ---
    > <initialState file="../20210211-0930.BASECASE/t0/outputs/finalState/outputState.dmp"/>
  disable the final IIDM dump (finalState), to save space
  set the desired log level ("DEBUG" is too verbose for a full contingency run)
Make sure that there is at least one disconnection event in both Astre and DynaWaltz
  this will become the reference for the disconnection time for all contingencies

## Slide 8: Summary for DynaWaltz (for Dynawo vs. Astre)
Example:
In bold, expected names (i.e. hard-coded)
The job file is a pattern ‘*JOB*.xml’
220210211-0930.BASECASE
├── Astre
│ └── donneesModelesEntree.xml
├── fic_JOB.xml
├── t0
│ ├── fic_CRV.xml
│ ├── fic_DYD.xml
│ ├── fic_IIDM.xml
│ └── fic_PAR.xml
└── tFin
├── fic_CRV.xml
├── fic_DYD.xml
├── fic_IIDM.xml
└── fic_PAR.xml

## Slide 9: Summary for DynaWaltz (for Dynawo vs. Dynawo)
For Dynawo vs. Dynawo, first perform all the steps as in the Astre vs. Dynawo case, and then:
Use the utility scripts convert_dwaltz2dwoAdwoB.sh to convert the case into a new subdirectory structure A / B:
Manually perform whatever changes are desired to case A and/or B